Quotation

ADULT DIAPER MACHINE Model XE-2018-DDF-SV

Подгузники для взрослых

| Name & Type of the machine | Unit | Quantity | Guangzhou Factory Price | Delivery Time | Place of Delivery |
| --- | --- | --- | --- | --- | --- |
| XE-2006-DDF | Set | One | ￥10，500，000. | 180days | Guangzhou |

  - BASIC SPECIFICATION

- Right handed machine  		Material flow from right to left

- Working speed				200 ppm

- Surface speed				250 m

- Efficiency: 				>85%

- Wastage: 					<3%

- Defibration capacity			15 kg.min

- Power Supply required		350 KVA, 380 V, 3 ph, 50 hz

- Air consumption			2000 L/min

- Air pressure				80 – 120 psi

- CE Safety standard

  - Mill – Dual fixed rotor mill for drum former with the following features

- 45kw electric motor

- Greased bearings with temperature readouts and alarm for overtemp

- Easy removal of breaker bar

- Carbide tip Chevron style rotor noise reduction style

- Pulp feed rolls on pneumatic nip for easy unjamming

- Pulp side guides and in feed tray

- Adjustable ventilation

- Two spindle unwind stand for pulp

1.3Dual Drum Forming core with the following features

- 3D Discrete pad formation to produce pads per attached drawings

- Quick changeover features between sizes

- Guaranteed total indicated run out of +- 2mm

- Guaranteed fluff weight variability of less than +- 5% from target

- Scarfing rolls – adjustable gapping

- Appropriate internal baffling for discrete forming

- Filter for filtration of process air including main fan and media cleaning fan.

- Forming fan

1.4SAP system

- Volumetric sap system for sap introduction into second drum former using compressed air

- Guaranteed pad to pad weight variability to not exceed 5% from target

- Sap nozzles with 3 coordinate adjustment to optimize distribution

- 15gram per product maximum capability

- Operator input for various pad weights

1.5 Calendar and Embossing

- Stepped calendar section for setting setting pad density

- Adjustable gap mechanism

- Feature to prevent excessive pad growth on discrete pad

- Adequate transfer plates between sections to assure pad integrity

- Emboss section for diamond pattern embossing Torque protection

- Torque protection and jam protection

1.6 Acquisition layer

- Cut and place acquisition layer applicator for placement on top sheet.

- Vacuum drum style with flex knife cutoff

- Separate dedicated vacuum fan

- Knife to have automatic oilers

- Torque protection

1.7 Leg elastic

- Elastic unwind stand with capability to run up to 8 strands of elastic on 12” diameter spools

- Spacing as per product drawings

- Easily adjustable mechanism for spacing adjustment from center line

- Glue heads applying adhesive directly to elastic

- Adhesive applicator to have one pump per head

1.8 Fastening Tape

- Qty four /product, vacuum drum style

- Separate dedicated vacuum fan for fastening tape unit

- Flex knife with knife oilers

- Tape unwind stand with tension adjustment

- Fingerlift sensor

- No tape detectors

- Open tape detectors

- Tape in wrong spot detectors

- Tape system to be easily adjustable for various product widths and lengths

- Glue heads applying adhesive directly to fastening tape

- Adesive applicator to have one pump per head

- Torque protection

1.9 Frontal Tape

- Qty one or two left and right separate per product

- Vacuum drum style cut and place application with positioning controlled.

- Separate dedicated vacuum fan for frontal tape

- Flex knife with knife oilers

- Dual unwind for split tape and independent tension control with auto splicing feature

- Unwinds to have 24” diameter capability with 3” I.D. cores

- Tape web break detection

- Torque protection

1.10 Inner leg gather

- Machine to have ribbon style Inner leg gather unit

- Total of two adhesive heads for elastic and two for ribbon attachment to top sheet with Mechanical Sealing unit.

- Elastic unwind capable of 4 strands with 12” diameter spools

- Easily adjustable head and strand bracketry with rules for operator documentation of good run settings

1.11 Leg Cutout die section

- Load pressure to be indicated

- Leg cutout vacuum fan

- Cutout receptacle for waste

- Die to have automatic oiler

- Torque protection

- Unit to have easily adjustable trim takeaway chutes for various product sizes

- Unit to be provided with the following dies and anvils

  - Two M/L dies

  - Two XL dies

  - Four anvils

1.12 Longitudinal fold

- Section to have adjustments with markings or rules for operator documentation and setup of good run settings.

- Folding rails to have adhesive release coatings.

1.13 Final knife

- Flex knife style with automatic knife oilers

- Torque protection

1.14 Cross folder

- Tri-fold

- Folding fingers to have adhesive release coatings

- Single reject station for out of spec products

- Torque protection

1.15 Unwinds

- All unwinds to be independently controlled with motors following main machine speed with a tension sensing devise (dancer) providing trim.

- Splicers have automatic feature with manual override

- All splices will be tape

- Splice detection photoeyes to see vendor splices and machine splices

- Web break detectors provided on all unwinds

- All webs to have automatic web guides properly designed before critical applications. Edge guides to keep web alignment within +- 1/8” of target

- Air shafts for cores – designed for 3” I.D. cores

- Stacker

- Stacker to be able to handle all products with a minimum of chain pitch changes

- Minimum count capability is (6) six

- Maximum count capability is (24) twenty four

- Quick change features

- Dual discharge with ability to work both together at same time from 2 exits, one for connecting the automatic packaging unit.

- Automatic packaging unit

- Packaging unit to be able to handle all products with a minimum of part changes

- Minimum count capability is (10) tem

- Maximum count capability is (24) twenty four

- Automatic bag feeding and sealing

- Automatic product in feeding with compress unit

- Speed Up to 20 cycles/min

- Quick change features

- Drive

Mitsubishi servo drives on all tooling and conveyors, Inverter drive unwinding system.

- Controls

- 24V DC control circuit.

- Power circuit according to the specification requirements of the end user.

- Mitsubishi PLC.

- E-stop lifeline running entire length of machine on operator and drive side.

- E-stop circuit hardwired into all E-stop pushbutton, guard doors and lifeline.

5   Operator control

- Provide hardwired E-stop mushroom style buttons at each operator station.

- Provide normal stop mushroom style buttons at each operator station.

- Mitsubishi touch screens for control of functions, setup and fault messaging.

6   Adhesive system

- Nordson/ITW Hotmelt system

- Every applicator head to have a dedicated pump or dual stream pump on dual applications

- Control of on/off and phasing to be accomplished through touch screen

- Manual purge, auto and off functions for all applications.

- The following applications are needed

  - Leg elastic gun

  - Leg elastic pump

  - Backsheet construction glue gun

  - Backsheet core construction glue pump

  - Topsheet construction – topsheet to core glue gun

  - Topsheet construction – topsheet to core glue pump

  - Acquisition layer - Topsheet construction glue gun

  - Acquisition layer - Topsheet construction glue pump

  - ILG elastic gun

  - ILG elastic pump

  - ILG ribbon to Topsheet gun

  - ILG ribbon to Topsheet pump

  - Frontal tape to backsheet construction glue gun

  - Frontal tape to backsheet construction glue pump

7   OEM components

- Web guides -BST

- Controls/drives –Mitsubishi main PLC, touch screens and Servos

- Photoeyes –SICK

- Bearings –SKF, FAG, PEER, UBC

- Pneumatics –FESTO, SMC, ARK

- Safet guard switches –Schmersal

- Timing belts –TB Woods HTD style metric, Bando, Optic belt, Goodyear

- Conveyor belts -Habasit

8   Spear Parts list for baby diaper machine:

| Item | QTY |
| --- | --- |
| Servo motors | 1 for each model |
| Servo Amplifer | 1 for each model |
| Cutting knife for end-cutting unit | 2 pcs |
| Cutting knife for fastening tape cut & place unit | 6 pcs |
| Cutting knife for frontal tape cut & place unit | 2 pcs |
| Cutting knife for ADL cut & place unit | 2 pcs |
| Conveyor belts | 1 set for each section |
| Timing belts | 1 set for each section |
| Stacking finger | 50 pcs |