塑料注射成型机

Plastic Injection Molding Machine

- 公司简介 Company introduction

山东通佳重工有限公司坐落在“孔孟之乡”的山东济宁国家高新技术产业开发区，占地20万平方米，是中国最大的绿色节能塑料中空成型机研发、生产基地和江北最大的伺服节能注塑机的研发、生产基地。

山东通佳重工有限公司是中国塑料机械工业协会副会长单位，中国轻工业协会理事单位，全国轻工系统技术创新先进单位，国家级高新技术企业，中国专利山东明星企业，国家级塑料成型装备工程技术中心。通佳产品被评为“山东名牌产品”。产品遍及全国各地和世界六十多个国家和地区。

“信任源于品质”，通佳重工凭借雄厚的企业综合实力，将不断提高产品质量，完善技术服务，更好的满足客户要求，携手国内外客户共创塑机产业的美好明天！

Shandong Tongjia Heavy Industry Co.,LTD locates in National High-tech Industrial Development Zone of Jining City, which is the hometown of Coufucius and Mencius, Shandong Province, The factory area is 200,000 square meters. The company is the largest research and development production base of green energy-saving Plastic Blow Molding Machine and the Series Servo Energy Saving Injection Molding Machine in north of Yangtze River.

Tongjia Heavy Industry is the vice-chairman of China Plastics Machinery Industry Association, the Director of China Light Industry Machinery Association, the Technological Innovation Enterprise among National Light Industrial and the High-new Technological Enterprise of State, Chinese Patent Shandong Famous Enterprise, been awarded ”Brand-name Products in Shandong Province”, products extend all over the national and over 60 countries and areas of the world.

“Trust is the result of quality”,based on strong comprehensive strength,Tongjia Heavy Industry will continuously improve product quality,perfect technical services to meet customer needs,hopes to create nice future of plastic machinery industry with clients from home and overseas.

- 公司荣誉Company honor

中国塑料机械工业协会副会长

The vice-chairman of China Plastic

Processing machine industry association

高新技术企业

The high-new technology enterprise

of Shandong Province

ISO9001:2000质量体系认证

ISO9001:2000 Quality system certification	                 CE认证CE certificate

- 车间展示Workshop Show

- 设备简介Machinery Brief

尊敬的客户  您好/ Dear Sir/Madam！

感谢您对我司的支持，现结合贵公司产品要求，将有关设备参数、配置提供给贵司，以供参考选择。

Thanks for your support and trust to Shandong Tongjia Heavy Industry Co.,Ltd. The equipment parameters, configuration in accordance with your requests as below, for your reference.

- 设备报价单Price List

| 项目Commodity | 规格Details | 数量 Quantity | 单价Unit юань КНР | 总价Total юань КНР |
| --- | --- | --- | --- | --- |
|  |  |  | 工厂人民币含税 with Vat in $ |
| 伺服节能注射机 ТПА Servo series Injection Molding Machine | TH220/SP | 3 Set（套） | 240000 | 720000 |
| 伺服节能注射机 ТПА Servo series Injection Molding Machine | TH320/SP | 1 Set（套） | 350000 | 350000 |
| 伺服节能注射机 ТПА Servo series Injection Molding Machine | TH400/SP | 1 Set（套） | 480000 | 480000 |
| 辅机：Auxiliary Machinery |
| 自动上料机Auto Feeder автоподача сырья | 300kg | 5 Set（套） | 2740 | 13700 |
| 干燥料斗 Plastic Dryer Сушилки | 100kg | 3 Set（套） | 4110 | 12330 |
| 干燥料斗 Plastic Dryer Сушилка | 150kg | 3 Set（套） | 4800 | 14400 |
| 冷水机Chiller холодильник | 20P | 2 Set（套） | 68500 | 137000 |
| 冷水机Chiller холодильник | 10P | 1 Set（套） | 35620 | 35620 |
| 破碎机Crusher дробилка | SP-600 | 1 Set（套） | 27400 | 27400 |
| 模具 Пресс-форма (матрица) | 0.36L | 1 | 123300 | 123300 |
|  | 0.5L | 2 | 123300 | 246600 |
|  | 3.3L | 1 | 123300 | 123300 |
|  | 5.5L | 1 | 123300 | 123300 |
|  | 10.7 | 1 | 44525 | 44525 |
| 模具（提手）Пресс-форма: ручки |  | 5 | 61650 | 308250 |
| 模具（盖子）Пресс-форма: крышка |  | 6 | 78775 | 472650 |
| 总价Total | 3232375 юаней КНР |

注：此报价基于EXW人民币含税价格，模具根据客户样品最终确定。

Please Note: The price based on EXW with vat in RMB, Mould was depended on your final product’s sample.

1.交货时间Delivery Time

双方确认合同中所有的技术和商务条款，并收到预付款后90工作日内交货。

Confirm the contract all the technical and commercial terms from both sides, and receive advance payment within 90 working days of delivery.

2.付款方式Payment Terms

收到30%预付款后合同生效，70%于交货前支付。

30% down payment by T/T , 70% by T/T before the delivery.

3.质量保证Quality guarantee

设备保修期一年。保修期内属设备制造本身质量引起的问题,由供方免费负责解决。但损坏的配件必须以旧换新,请用户全力配合。

The machine is guaranteed for one year .During the period of guarantee, the seller will solve the problem caused by the machine itself for free. But for the damage of other spare components, the buyer should cooperate with the seller.

4.售后服务After sale service

我方派两名工程师来买房工厂安装调试机器。买房应该负责工程师伙食，住宿和在买方国家的

一切正常开销,买方负责工程师的签证费，来回机票和每天的调试安装费用。

We send two Engineers to buyer's company to do installation and training. The buyer should be responsible for food and hotel（at least three star hotel) and other necessary expense in local. The buyer will bear the Engineer’s visa cost, flights and commissioning cost.

- 设备性能特点Performance Characteristics

(1) 锁模部件Clamping parts

1>合模部分采用先进的斜排五支点增力型结构，合模部分刚性好。

Reliable 5-point twin –toggle locking mechanism, Platens are designed

Under Finiter-Element Analysis.

2>高速闭模稳定性好，低压模保准确。

High speed clamping is stable while low pressure protection is accurate.

3>采用自动定量润滑系统，配合自动缺油报警装置，顶出行程采用位移

传感器控制，行程精确可靠，有多种顶出方式可供选择

Automatic quantitative lubrication system ，oil shortage alarm ，Ejector

stroke precisely controlled by transducer ，plenty of  ejector modes  for you to choose.

(2) 注射部件Injection parts

1>注射部分采用双杠平衡式注射系统

Double-cylinder balance injection system

2>注射控制采用位移传感器实现精确的注塑重量控制

Shot weight is precisely controlled by transducer .

3>预塑采用五星马达，可以实现无极调速

Using hydraulic motor to carry out variable speed.

(3) 驱动部分Drive Unit

1>伺服驱动系统采用国际知名品牌驱动器

Using famous server driver.

2>配以优化的闭环控制算法，实现节能的最大化

Special close loop calculated solution best energy saving

(4) 控制部分Control Unit

1>电气控制系统采用进口注塑机专用控制系统

Special controller for plastic injection molding machine .

2>主要元件采用国外知名公司配件，如法国TE,意大利Gerfran等

All the main components are imported from famous

company For examples :TE(France), Gefran(Italy) etc.

- 设备基本参数Technical Data for Model TH220/SP

| 项 目 | 单位 | TH220/SP |
| --- | --- | --- |
| ITEMS |  |  |
| 注射装置INJECTION UNIT | 螺杆直径 диаметр шнека | Screw Diameter | mm | 50 |
|  | 螺杆长径比 соотношение длины к диаметру | Screw L/D Ratio | L/D | 20.0 |
|  | 理论容量 объём расчётный | Shot Size(Theoretical) | cm3 | 445 |
|  | 注射重量（Ps）вес впрыска | Injection Weight | g | 405 |
|  | 注射压力 давление | Injection Pressure | Mpa | 192.7 |
| 合模装置CLAMPING UNIT | 合模力 сила форморки | Clamping Force | KN | 2200 |
|  | 移模行程 ход, расстояние | Clamping Stroke | mm | 540 |
|  | 拉杆内距 внутреннее расстояние | Space Between Tie Bar | mm | 530×530 |
|  | 最大模厚 макс толщина матрицы | Max. Mold Height | mm | 560 |
|  | 最小模厚 мин толщина матрица | Min. Mold Height | mm | 220 |
|  | 顶出行程 ход выдавливания | Eject Stroke | mm | 150 |
|  | 顶出力 сила толкания | Eject Force | KN | 68 |
|  | 顶出杆根数 кол-во толкателей | No. Of Ejector Pins | piece | 9 |
| 其它OTHERS | 最大油泵压力 макс давление масляной помпы | Max. Pump Pressure | MPa | 17.5 |
|  | 油泵马达 мощность помпы | Pump Motor Power | KW | 22/28 |
|  | 电热功率 | Heat power мощность нагревательных элементов | KW | 12.8 |
|  | 料斗容积 | Hopper Capacity вес бака сырья | Kg | 50 |
|  | 外形尺寸 | Dimensions размер | M | 5.5×1.5×2.2 |
|  | 油箱容积 | Oil Tank Capacity объём масляного бака | L | 400 |
|  | 重量 | Machine Weight вес масляного бака | T | 6.8 |

- 设备基本参数Technical Data for Model TH320/SP

| 项 目 | 单位 | TH320/SP |
| --- | --- | --- |
| ITEMS |  |  |
| 注射装置INJECTION UNIT | 螺杆直径 | Screw Diameter | mm | 60 |
|  | 螺杆长径比 | Screw L/D Ratio |  | 20.0 |
|  | 理论容量 | Shot Size(Theoretical) | cm3 | 780 |
|  | 注射重量（Ps） | Injection Weight | g | 710 |
|  | 注射压力 | Injection Pressure | Mpa | 192.5 |
| 合模装置CLAMPING UNIT | 合模力 | Clamping Force | KN | 3200 |
|  | 移模行程 | Clamping Stroke | mm | 650 |
|  | 拉杆内距 | Space Between Tie Bar | mm | 630×630 |
|  | 最大模厚 | Max. Mold Height | mm | 650 |
|  | 最小模厚 | Min. Mold Height | mm | 250 |
|  | 顶出行程 | Eject Stroke | mm | 160 |
|  | 顶出力 | Eject Force | KN | 68 |
|  | 顶出杆根数 | No. Of Ejector Pins | piece | 13 |
| 其它OTHERS | 最大油泵压力 | Max. Pump Pressure | MPa | 17.5 |
|  | 油泵马达 | Pump Motor Power | KW | 30/41 |
|  | 电热功率 | Heat power | KW | 19.2 |
|  | 料斗容积 | Hopper Capacity | Kg | 50 |
|  | 外形尺寸 | Dimensions | M | 6.4×1.7×2.4 |
|  | 油箱容积 | Oil Tank Capacity | L | 700 |
|  | 重量 | Machine Weight | T | 10.5 |

- 设备基本参数Technical Data for Model TH400/SP

| 项 目 | 单位 | TH400/SP |
| --- | --- | --- |
| ITEMS |  |  |
| 注射装置INJECTION UNIT | 螺杆直径 | Screw Diameter | mm | 70 |
|  | 螺杆长径比 | Screw L/D Ratio |  | 22.0 |
|  | 理论容量 | Shot Size(Theoretical) | cm3 | 1348 |
|  | 注射重量（Ps） | Injection Weight | g | 1225 |
|  | 注射压力 | Injection Pressure | Mpa | 191.3 |
| 合模装置CLAMPING UNIT | 合模力 | Clamping Force | KN | 4000 |
|  | 移模行程 | Clamping Stroke | mm | 750 |
|  | 拉杆内距 | Space Between Tie Bar | mm | 730×730 |
|  | 最大模厚 | Max. Mold Height | mm | 750 |
|  | 最小模厚 | Min. Mold Height | mm | 280 |
|  | 顶出行程 | Eject Stroke | mm | 200 |
|  | 顶出力 | Eject Force | KN | 125 |
|  | 顶出杆根数 | No. Of Ejector Pins | piece | 13 |
| 其它OTHERS | 最大油泵压力 | Max. Pump Pressure | MPa | 17.5 |
|  | 油泵马达 | Pump Motor Power | KW | 51/60 |
|  | 电热功率 | Heat power | KW | 26.4 |
|  | 料斗容积 | Hopper Capacity | Kg | 50 |
|  | 外形尺寸 | Dimensions | M | 7.96×1.96×2.48 |
|  | 重量 | Machine Weight | T | 14.7 |
|  | 油箱容积 | Oil Tank Capacity | L | 800 |

注：以上数据仅供参考，本公司保留元件及机械结构更改权，购买设备涉及的有关内容以合同为准。

Note: The above-mentioned data is only for your reference and we keep the rights for modification of the component and machinery structure, the relevant contents involved in equipment purchase should be subject to the contract.

- 辅助设备(选购)Assistant machines（choose to buy）

1>自动上料机Automatic Feeder

| 型号Model (kg/h) | 容量Capacity (L) | 产量Capacity (kg/h) |
| --- | --- | --- |
| 300 | 6 | 300 |
| 700 | 6 | 350 |

2> 塑料混合机Plastic Mixer

| 型号Model (kg/time) | 功率Power (KW) | 尺寸Dimension (cm) |
| --- | --- | --- |
| 100 | 3 | 100*100*125 |
| 150 | 4 | 115*115*130 |
| 200 | 5.5 | 120*120*150 |

3> 塑料破碎机Plastic Crusher

| 型号Model (kg/h) | 功率Power (KW) | 产量capacity (kg/h) |
| --- | --- | --- |
| TJ-PS300 | 5.5 | 200~300 |
| TJ-PS400 | 7.5 | 300~400 |
| TJ-PS500 | 11 | 400~600 |
| TJ-PS600 | 15 | 500~800 |

4> 冷水机Chiller

| 型号Model | 冷却方式 Cooling way | 水泵功率 Water pump power (KW) | 压缩功率 Compressor power (KW) |
| --- | --- | --- | --- |
| 10P | Water cooling | 0.75 | 7.5 |
|  | Air cooling |  |  |
| 20P | Water cooling | 2.2 | 15.5 |
|  | Air cooling |  |  |

5> 料斗干燥机Drying hopper

| 型号Model Kg/h | 干燥电机功率 Drying motor power (KW) | 吹风电机功率 Blowing motor power (KW) |
| --- | --- | --- |
| 100 | 6 | 250 |
| 200 | 12 | 350 |

6>螺杆式空压机Screw compressor

| 型号Model | 功率Power (KW) | 外形尺寸 Dimension(mm) |
| --- | --- | --- |
| 10A | 7.5 | 900×700×1040 |
| 15A | 11 | 1060×800×1230 |
| 20A | 15 | 1060×800×1230 |

- 电器配置（仅供参考）Main Configuration（only for reference）

| 序号No. | 电器Electrical Appliance | 品牌Brand |
| --- | --- | --- |
| 1 | 电子尺 Electronic ruler | 杰弗伦（意大利）Gerfran(Italy) |
| 2 | 空气开关 Air Switch | 施耐德（法国）Schneider(France) |
| 3 | 限位开关 Limit Switch | 施耐德（法国）Schneider(France) |
| 4 | 电眼Electric eye | 阳明（台湾）Fotek(Taiwan) |
| 5 | 接触器 Contactor | 施耐德（法国）Schneider(France) |
| 6 | 电脑 Computer | 弘讯（台湾）Techmation(Taiwan) |
| 7 | 齿轮泵 Gear Pump | 艾克勒（法国）/桑尼斯（美国） Eckerle(France)/ Sunny(USA) |
| 8 | 伺服电机 Servo Motor | 汇川（中国）/蒙德（中国） Inovance(China)/Mund(China) |
| 9 | 伺服驱动器 Servo driver | 汇川（中国）/蒙德（中国） Inovance(China)/Mund(China) |
| 10 | 压力传感器 Pressure Sensor | 丹弗斯（丹麦）Danfoss(Denmark) |
| 11 | 电磁换向阀 Solenoid Directional Valve | 油研（日本）Yuken(Japan) |
| 12 | 高压胶管 High-pressure Hose | 阿法格玛（意大利）Alfagomma(Italy) |
| 13 | 电压基于Volt based on: 380V，3 phase, 50Hz. |

- 随机配件（仅供参考）Main Spare parts（only for reference）

| 序号No. | 项目Items | 序号No. | 项目Items |
| --- | --- | --- | --- |
| 1 | 加长喷嘴 Lengthening Nozzle | 12 | 密封圈 Seal Ring |
| 2 | 喷嘴扳手 Nozzle Spanner | 13 | 不锈钢加热圈 Stainless Steel Heating Ring |
| 3 | 止逆环 Non-return valve | 14 | 陶瓷加热圈 Ceramic Heating Ring |
| 4 | 密封环 Sealing loop | 15 | 热电偶 Thermocouple |
| 5 | 模具压板 Mould Platen | 16 | 接近开关 Approximate Switch |
| 6 | 滑块 Slide Block | 17 | 限位开关 Limit Switch |
| 7 | 螺丝 Screw | 18 | 固态继电器 Solid Relay |
| 8 | 平垫 Flat Mat | 19 | 中间继电器 Middle Relay |
| 9 | 机身调平栓 Body Balance Bolt | 20 | 黄油枪 Butter Gun |
| 10 | 六角扳手 Hexagonal Spanner | 21 | 尼龙管 Nylon Hose |
| 11 | 螺丝刀 Screwdriver | 22 | 油管接头Oil Tube Joint |